## Slide 1
Linear Algebra / Solid Mechanics Review
Matrix Algebra - Appendix A
Solving Systems of Linear Equations - Appendix B
Solid Mechanics Theory - Appendix C, CVE 220 & MCE 301 texts

## Slide 2: Review – Matrix Algebra
We will see that the finite element method requires solving large systems of linear equations using matrix algebra tools.
First, review matrix multiplication
In general
2x2
2x3
2x3
[A] [B] = [C]
n x p
m x n
m x p

## Slide 3: Review – Matrix Algebra (see Appendix A)
To review some basic matrix algebra, consider the following system of equations
or
(x,y)= (1,4)

## Slide 4: Matrix Algebra (cont.)
Matrix form:
Matlab code
    a=[2 1;1 4]
    b=[6;17]
    determinant=det(a)
    solution=a\b
Matlab output
  a =
  2 1
  1 4
  b =
  6
  17
  determinant =
  7
  solution =
  1.0000
  4.0000
Note |a|  0

## Slide 5: Matrix Algebra (cont.)
Now consider a different system of equations
or

## Slide 6
a =
4 2
2 1
b =
16
6
determinant =
0
Warning: Matrix is singular to working precision.
solution =
Inf
-Inf
Matrix Algebra (cont.)
Matrix form:
a=[4 2;2 1]
b=[16;6]
determinant=det(a)
solution=a\b
Note |a| = 0
Matlab code
Matlab output

## Slide 7: Matrix Algebra (cont.)
System of three equations (Matlab format)
Code:
  a=[-1 1 2;3 -1 1;3 3 1]
  b=[2;6;2]
  solution=a\b
Output:
  a =
  -1 1 2
  3 -1 1
  3 3 1
  b =
  2
  6
  2
  solution =
  1
  -1
  2

## Slide 8: Matrix algebra applied to FEA
For displacement based stress analysis
Stiffness matrix - Symmetric since Kij = Kji
Nodal Displacements
Nodal Forces

## Slide 9: Other Matrix Terminology
Banded matrix
  If all non-zero terms are contained within a band along the diagonal, the matrix is said to be banded
Sparse matrix
  If a matrix has relatively few non-zero terms (as is common in FEA), the matrix is said to be sparse
Singular matrix
  If the determinant of the matrix equals zero, the matrix is said to be singular. As we saw, if [A] is singular, then the system of equations [A]{x}={b} has no unique solution.

## Slide 10: Other Matrix Terminology (cont.)
Transpose
  The transpose of a matrix is found by interchanging rows and columns, e.g.
  Transpose of a product

## Slide 11: Review – Solution of Linear Algebraic Equations (see Appendix B)
Problem B.4 (p. 866)
Gaussian Elimination - Example
Solved by hand in class

## Slide 12
Solution of Linear Algebraic Equations (cont.)
Alternate – solve using Matlab
>> A=[2 1 -3;4 -2 3; -2 2 -1]
A =
2 1 -3
4 -2 3
-2 2 -1
>> b=[11;8;-6]
b =
11
8
-6
>> Ainv=inv(A)
Ainv =
0.1818 0.2273 0.1364
0.0909 0.3636 0.8182
-0.1818 0.2727 0.3636
>> A*Ainv
ans =
1.0000 0 0
0.0000 1.0000 -0.0000
-0.0000 0.0000 1.0000
>> Ainv*A
ans =
1.0000 0 0
-0.0000 1.0000 -0.0000
-0.0000 0 1.0000
>> det(A)
ans =
-22
>> x=A\b
x =
3
-1
-2
>> A*x
ans =
11
8
-6

## Slide 13
Solid Mechanics (Elasticity) Theory (see Appendix C, CVE 220 & MCE 301 texts )

## Slide 14
Equilibrium (2D Stress States)

## Slide 15
Equilibrium (3D Stress States)

## Slide 16
Displacement and Strains
Displacement vector
Strain components

## Slide 17
Elastic Material Properties – Uniaxial Tension
Young’s modulus, E
Poisson’s ratio, 

## Slide 18
Elastic Material Properties – Torsion (Pure Shear)

## Slide 19
Multiaxial Stress States – Hooke’s Law
[D] - Constitutive Stiffness matrix (6X6)

## Slide 20
Multiaxial Stress States – Hooke’s Law
(cont.)
Constitutive Compliance Matrix (6X6) = [D]-1

## Slide 21
Beam Bending
Moment-curvature () relation
Moment of Inertia (rectangular cross-section)

## Slide 22
Structural Stiffnesses
Axial Stiffness
Torsional Stiffness
Bending Stiffness